Invitation to Bid

Sealed bids will be received by the City of Valley Falls, Kansas at the office of the City Clerk, Valley Falls until 5:00 p.m. May 15, 2020 and then opened at 6:30 p.m.  The bid shall be for furnishing all labor and materials and for performing all work for the two (2) inch mill and overlay of the specified street.

1.) OVERLAY OF ASPHALT on existing street and driveways and street extensions on the following streets:

A.) Clean the existing street and apply tack oil, construct a two (2) inch thick asphalt mill/overlay on street from curb to curb shown as “A” on the city map.  – On Walnut Street from 16 Highway to 12th St.  There are six (6) places at intersections and one driveway entrance that will need milled down.  The places to be milled are marked out on the included map.  The milling should go from nothing to 2” deep in 6’ at all milling location and be the width of the intersection or driveway. There will be 4” full-depth patching as needed.

*	The City of Valley Falls will be providing a dump site for the asphalt millings.

*	The contractor should verify all measurements, The City of Valley Falls is not liable for these measurements in the bid document, and they are only an estimate.

*	The City of Valley Falls reserves the right to increase or decrease these quantities with the expressed understanding that NO adjustment in unit bid price will be allowed.

*	The City of Valley Falls requires that the work be complete prior to August 15, 2020 or have written approval from the City Administrator to extend the date due to natural causes.

All bids are to be submitted to the City office of Valley Falls, Kansas.  Copies of the specifications and other documents are on file in the office of the City Clerk, Valley Falls, Kansas, and are open for public inspection during normal office hours.  Proposals shall be submitted in sealed envelopes addressed the City of Valley Falls, 2020 Street Improvements, 417 Broadway street, Valley Falls, Kansas 66088.  Bids received after closing time will be returned unopened.

The City of Valley Falls, Kansas, reserves the right to reject any or all bids and to waive informalities.